## Slide 1: Memory-Efficient Object Detection Using Ultrasonic Rangefinders On The DE2Bot
Sushanth Penta
Eric Rafalovsky
Antony Samuel
Leo Weng
Digital Design Laboratory - ECE 2031 L01
Georgia Institute of Technology
11/29/2016

## Slide 2: Project Description
Utilize the DE2Bot to autonomously locate up to 6 objects in an arena
“Tag” these objects within a 120 second timeframe
Return to a 2 by 2 foot home square after tagging each object
Sample Arena Layout
12 feet
8 feet

## Slide 3: Design Overview
Reset Position
Object Detected
Begin Search Process
Tag Object

## Slide 4: Design Implementation
Implemented through SCOMP assembly software
Primary Subroutines

## Slide 5: Detecting Objects
Sonars at ± 90° and ± 12°, updating at 6.25 Hz, used for object detection
  Checking left, right and directly in front of robot
Splitting the arena in two minimizes threshold distance, minimizing error due to the conical shape of sonars
  3.5 foot detection threshold for ± 90° sonars

## Slide 6: Tagging Objects
Sonars at ± 12°, updating at 12.5 Hz, used for object tagging
Tagging threshold of 170 mm
  Threshold calculated using the known constant deceleration of the DE2Bot
Object is lightly tagged to minimize odometry error

## Slide 7: Returning Home
Odometry used to reverse robot actions
Traveled path is free from obstruction so the robot can return home at high speed

## Slide 8: Achieving Multiple Robot Runs
Robot manually repositioned in home square after it returns
Odometry module reset through button press
  Mechanism of delaying the robot while human is in the arena

## Slide 9: Minimizing Odometry Error
DE2Bot only travels straight (parallel to either of the arena walls)
DE2Bot only makes 90° turns
DE2Bot avoids pushing arena objects
Odometry is reset before each run
Odometry is only used to return home following object tagging
  Able to return to home square without wall collision >70% time

## Slide 10: Challenges Encountered
Tagging objects without pushing them
  Tag the object lightly by beginning to decelerate at a calculated distance
Turning the robot 90° accurately and precisely
  Combinations of wheel speeds and timings were tested for the most accurate result

## Slide 11: Results
Implemented in only 303 words. 15% of the default SCOMP memory
 | Run 1 | Run 2 | Average
Objects Tagged | 4 | 0 | 2
Returned Home | 0 | 0 | 0
Collisions/Pickups | 5 | 0 | 2.5
Demonstration Results

## Slide 12: Design Strengths and Weakness
Strengths
Robot is able to return home at high speed due to known empty path
Average distance from sonar to detected objects is minimized
Little reliance on odometry during detection
Low memory requirements due to lack of mapping
Weaknesses
Non-direct path to tagging objects
Non-direct path back to the home square
  Up to 38% less efficient than direct path

## Slide 13: Future Work
Implement basic mapping of the arena to allow for:
  More direct object tagging
  More direct return home